## Slide 1: Scenario Analysis of PT-HWR Used Fuel Management for Once-Through Thorium Fuel Cycles
Daniel Wojtaszek
2nd Technical Workshop on Fuel Cycle Simulation
July 19, 2017
Notes: For best results, please send the large top image to the back layer. Choose “Arrange” then select “Send to Back”.

## Slide 2: Presentation Outline
Objective
Pressure Tube Heavy Water Reactor (PT-HWR)
Thorium-Uranium Fuel Concepts
Analysis Methodology
Results
Conclusions / Future Work
Discussion

## Slide 3: Objective
To analyze some potential impacts on the management of used fuel associated with deploying thorium fuels in PT HWRs in a once through fuel cycle.
This analysis is focused on dry storage and the deep geological repository (DGR).

## Slide 4: Pressure Tube Heavy Water Reactor
Heavy water moderated and cooled,
High neutron economy
Current PT-HWRs are fuelled with natural uranium (NU)
Online refuelling
Fuel is in the form of cylindrical fuel bundles
  (~0.5 m long, ~0.1 m diameter)

## Slide 5: Thorium-Uranium Fuel Concepts
Low-NU
100% NU
BU ~7.1 MWd/kg
Core Mass ~86 MTHE
Med-SEU+Th
Centre element (red): 100% Th
Ring elements (green): 98% SEU + 2% Th
BU~19.1 MWd/kg
Core Mass ~86 MTHE
SEU: Slightly Enriched Uranium (1.2 wt% 235U/U)
LEU: Low Enriched Uranium (5 wt% 235U/U)
Hi-LEU/Th
Graphite Centre Element (grey)
Ring elements (green): 50% LEU / 50% Th
BU~40.6 MWd/kg
Core Mass ~60 MTHE

## Slide 6: Analysis Methodology (pt. 1)
Fuel Depletion and Decay Calculations
(WOBI)
Calculate Used Fuel Discharge
Annually discharged used fuel (kgHE/year)
Core fuel mass discharged at reactor end of life
Decay power of used fuel each year after discharge
PT-HWR Assumptions
Thermal efficiency: 33%
Capacity Factor: 85%
Reactor Lifetime: 30 years
Reactor Power
Fuel Burnup
Decay power
Core Fuel Mass
Scenario Assumptions
Installed Capacity: ~13.5 GWe
Fleet operation: 2025 - 2085

## Slide 7: Analysis Methodology (pt. 2)
Used Fuel Mass Flow
Reactor
↓
Wet storage
↓
Dry storage
↓
DGR
(Spreadsheet)
Used Fuel Discharge
Scenario Assumptions
Wet storage duration: 5 years
Minimum used fuel age for DGR: 30 years
Dry Storage Assumptions
(MACSTOR)
Max number of Fuel bundles/basket: 60
Max decay power/basket: 0.36 kW
DGR Assumptions
(Canadian Concept)
Max number of Fuel bundles/container: 360
Max decay power/container: 1.3 kW
Max number of containers loaded/year: 370
First year of operation: 2060
Annually discharged used fuel (kgHE/year)
Core fuel mass discharged at reactor end of life
Decay power of used fuel

## Slide 8: Results: Wet Storage
Chart: Year

## Slide 9: Results: Dry Storage
Chart: Year

## Slide 10: Results: DGR
Chart: Year

## Slide 11: Conclusions
PT-HWRs are a viable existing technology for utilizing thorium-based fuels and uranium-based fuels augmented by small amounts of thorium.
Higher-burnup fuels can result in lower wet-storage requirements, but higher dry-storage requirements.
Ultimately, higher-burnup SEU+Th and LEU/Th fuels can have lower DGR requirements than NU.

## Slide 12: Future Work: Multi-Stage Fuel Cycles
Stage 1
Stage 2
Stage 3
LWR LEU
PT-HWR Pu+Th
Pu
PT-HWR LEU+Th
PT-HWR 233U+Th
233U
233U
LWR LEU
FR Pu+235U+Th
Pu
PT-HWR 233U+Th
233U
PT-HWR 233U+Th
233U
Pu

## Slide 13: Thank you
Questions?
Daniel Wojtaszek
daniel.wojtaszek@cnl.ca
Notes: For best results, please send the large top image to the back layer. Choose “Arrange” then select “Send to Back”.
This slide is not available in the Master. To add slides to you deck, simply duplicate the slide itself.